coalescing_unrolled_spacing_vs_unrolled_group_and_spacing.png
Unrolled Spacing
unroll the inner loop such that “spacing = i” performs i reads per loop iteration
- “spacing = 0” performs 1 reads per loop with contiguous parallel reads
- “spacing = 1” performs 2 reads per loop iteration, with noncontiguous (separated by 1 entry / 16 bytes) parallel reads
- Question: Why does spacing = 1 outperform spacing = 0? Is it because loop overhead is more costly than increased number of reads per global memory transaction?

Unrolled Group and Spacing
- unroll the inner loop and the global work size (128) of the outer loop, such that “spacing = i” performs 128*(i + 1) reads per loop iteration
- “spacing = 0” performs 128 reads per loop with contiguous parallel reads
- “spacing = 1” performs 256 reads per loop iteration, with noncontiguous (separated by 1 entry / 16 bytes) parallel reads
- spacing = 0 now performs best as expected, like due to reduced loop overhead
- everything performs worse however, likely due to increased instruction cache misses

Summary:
- Degradation in performance is likely due to increased instruction cache misses (loop unrolling is a trade off between reducing comparison operations, and increasing instruction cache misses)
- Possible use in the future would be to modify the encryption/decryption algorithms and unroll a portion of the encryption loop based on a sufficiently small factor of the encryption input (probably at most the page size, but more likely smaller than that since otherwise we would get the degradation observed here).